## Slide 1: Ludlow Village: NH Deck(49) Bridge Rehabilitation Town Highway 1 (Main St.) – Bridge #26 over Jewell Brook
December 2, 2019

## Slide 2: Introductions
JB McCarthy, P.E.
VTrans Design Project Manager
Gary Sweeny, P.E.
VTrans Design Engineer

## Slide 3: Purpose of Meeting
Provide an understanding of our approach to the project
Provide an overview of existing conditions
Discuss the proposed project and traffic control
Provide an opportunity to offer input on the project.
Provide an opportunity to ask questions and voice concerns

## Slide 4
Bridge 26
Project Location
Project Location

## Slide 5
Project Location

## Slide 6: Description of Terms Used

## Slide 7
Existing Conditions – Bridge #26
Roadway Classification – Principal Arterial, National Highway System
Bridge Type – 47’ Single Span, Rolled Beam, with Concrete Deck
Ownership – Township of Ludlow
Constructed in 1931, Rebuilt in 1965
Looking West on Main St. over Bridge

## Slide 8
Bridge #26 - 2019 Rating:
Deck Rating: 5 (Fair)
Superstructure Rating: 7 (Good)
Substructure Rating: 6 (Satisfactory)
Channel Rating: 8 (Very Good)

## Slide 9
The bridge is in fair condition:
  Random spots of advanced deck deterioration
  The deck in beam bay 4 has the potential for a hole
Damaged and substandard aluminum pedestrian rail should be upgraded
Existing Conditions – Bridge #26

## Slide 10
Approaches
Existing Conditions - Bridge #26

## Slide 11
Existing Conditions
Jewell Brook Looking Upstream

## Slide 12
Existing Conditions - Bridge #26

## Slide 13
Existing Conditions - Bridge #26

## Slide 14
Existing Conditions - Bridge #26

## Slide 15
Existing Conditions - Bridge #26

## Slide 16: Proposed Project - Bridge #26
Bridge Deck and Superstructure Replacement with Traffic Maintained on one lane in each direction
TH-1 (Main St.) Bridge Typical Section
  12’ Travel Lanes/10’ Shoulders/5’-0” Sidewalk/Combination Concrete/Steel Tubing Guardrails

## Slide 17: TH-1 (Main St.) Proposed Typical Section
6’6” 10’ 12’ 12’ 10’ 6’6”

## Slide 18: Existing Layout

## Slide 19: Proposed Roadway Profile

## Slide 20: Construction Phase 1

## Slide 21: Construction Phase 2

## Slide 22
Phased Construction
Proposed Maintenance of Traffic
Existing Conditions

## Slide 23
Phased Construction
Proposed Maintenance of Traffic
Phase 1

## Slide 24
Phased Construction
Proposed Maintenance of Traffic
Phase 2

## Slide 25
Phased Construction
Proposed Maintenance of Traffic
Final Condition
6’6” 10’ 12’ 12’ 10’ 6’6”

## Slide 26: Project Summary
Bridge Deck and Superstructure Replacement
Traffic Maintained on one lane in each direction.
Town share to be 5%
TH-1 (Main St.)
  12’ Travel Lanes/10’ Shoulders/5’-6” Sidewalk/Concrete Barrier with Steel Tubing Guardrail

## Slide 27: Preliminary Project Schedule
Target Construction Schedule (2022):
  May 1 Work Begins
  June 1 Temporary Traffic Pattern in place Phase 1
  August 1 Phase 1 Complete
  August 1 Temporary Traffic Pattern in place Phase 2
  October 1 Normal Traffic Pattern Resumes
  November 1 Project Complete

## Slide 28: Preliminary Project Budget
Conceptual Level Budget Estimate
  Construction Cost: $1,615,000
  (including Contingencies and
  Construction Engineering)
  Preliminary Engineering Costs: $210,000
  Right of Way: $25,000
  Conceptual Project Cost Estimate: $1,850,000
  Town Share 5% - Approximately $92,500

## Slide 29: Town Considerations
Confirm Scope of Project
Replacement deck and superstructures one half at a time while maintaining two lanes of traffic.

## Slide 30: Town Considerations
How will truck traffic on VT 100 be handled? How is it handled now?

## Slide 31: Truck Movements – Northbound

## Slide 32: Truck Movements - Northbound

## Slide 33: Truck Movements - Southbound

## Slide 34: Truck Movements - Southbound

## Slide 35: Town Considerations
Describe floods experienced at the site.

## Slide 36: Town Considerations
Does the ROW look correct?

## Slide 37: Town Considerations
Confirm bicycles to transit work zone in travel lanes.

## Slide 38: Town Considerations
Pedestrian passage during construction

## Slide 39: Town Considerations (contin)
Confirm proposed Bridge Rail.

## Slide 40: Town Considerations (contin)
Confirm general project schedule – May through October.

## Slide 41: Town Considerations (contin)
Confirm treatment of original rail pieces and light poles (ie remove, preserve, and re-install).

## Slide 42: Next Steps
Town confirms Items of Discussion at this meeting
Town signs Finance and Maintenance Agreement
Vtrans moves into Conceptual Design Phase

## Slide 43: Ludlow Village: NH Deck (49) Questions and Comments TH-1 (Main St.) – Bridge #26 over Jewell Brook
September 2019
For more information:
https://outside.vermont.gov/agency/vtrans/external/Projects/Structures/18j009

## Slide 44: Proposed Project - Bridge #26
Bridge Deck and Superstructure Replacement with Traffic Maintained on two lanes in each direction
VT100 Typical
  11’ Southbound Lane/1’ Shoulder
  10’Northbound Lane/2’ Shoulder
TH-1 (Main St.) Bridge Typical
  12’ Travel Lanes/10’ Shoulders/5’-0” Sidewalk/Combination Concrete/Steel Tubing Guardrails
VT 103 Typical
  12’ Travel Lanes/10’ Shoulders/5’-6” Sidewalks

## Slide 45: VT 100 Proposed Typical Section

## Slide 46: Regional Detour Route on State Owned Roads 26.5 Mile Trip

## Slide 47: Design Criteria and Considerations
Traffic Data for VT 103 and VT 100 as of 2018
Speed Limit 30 mph
Source of data:
https://vtrans.ms2soft.com/tcds/tsearch.asp?loc=Vtrans&mod=

## Slide 48: Maintenance of Traffic Options Considered
Offsite Detour
Temporary Bridge
Phased Construction

## Slide 49
Location Map
Ludlow Village Bridge 26

## Slide 50
Phased Construction
Proposed Maintenance of Traffic